## Slide 1
Reinforcement Learning for Thrust-Vectored Fin Control of an EDF VTOL Vehicle
PPO-Based Attitude and Position Control in GPU-Accelerated Simulation
Tang Zijian (Jacob Tang)
Department of Applied Data Science Minnesota State University, Mankato
AI Conference 2026
[Insert EDF Drone Photo / CAD Render]
1/17

## Slide 2
Presentation Outline
2/17
1
Motivation & Problem Statement
Why thrust-vectored EDF drones?
2
Vehicle Platform & Control Architecture
The physical testbed
3
Simulation Environment
GPU-accelerated Isaac Sim setup
4
Physics Models
Propulsion, aerodynamics, actuators
5
PPO Algorithm & Training
Observations, actions, reward design
6
Experimental Results
Hover & landing performance
7
Discussion & Future Work
Challenges and next steps
~20 minute presentation
Key Takeaway
Can deep RL learn to control a vehicle that steers by deflecting fins in its own exhaust stream? Yes — PPO achieves 100% landing rate with soft touchdowns in simulation, opening the door to sim-to-real transfer on a physical drone testbed.

## Slide 3
Motivation: Why Thrust-Vectored EDF Drones?
3/17
THE CONTROL CHALLENGE
● Conventional multirotors: independent rotor speeds → decoupled control
● Thrust-vectored EDF: single thrust source + 4 jet-vane fins
● Fin effectiveness ∝ throttle² — at 50% throttle, only 25% authority
● Nonlinear aerodynamics, actuator lag, gyroscopic precession
● Classical linear controllers (PID/LQR) limited to narrow operating envelope
● RL can learn the full nonlinear mapping end-to-end
Why It Matters
● Aerodynamic efficiency over multirotors
● Noise reduction (single fan vs. 4+ rotors)
● Mechanical simplicity for certain missions
● Applicable to rocket landing (jet vanes)
The Core Coupling
F_fin = q · S · C_N(α) where q ∝ throttle² → Reducing throttle to descend simultaneously reduces your ability to steer laterally

## Slide 4
Related Work & Research Gap
4/17
RL for Aerial Vehicles
● Hwangbo et al. — PPO for agile quadrotor control
● Koch et al. — Deep RL for attitude control
● Pi et al. — Sim-to-real under wind disturbances
● GPU-parallel training (Isaac Gym, Rudin et al.)
Thrust Vector Control
● Long history in rocketry (gimbaled nozzles)
● Jet-vane TVC for VTOL vehicles
● Classical: PID/LQR around hover linearization
● Limited operating envelope for nonlinear regime
Sim-to-Real Transfer
● Domain randomization (Tobin et al.)
● System identification (Yu et al.)
● CAD2RL: simulation-only to real flight
● Fidelity of dynamics model is critical
RESEARCH GAP
RL for thrust-vectored fin control of EDF vehicles remains largely unexplored. Key distinctions: single thrust source with coupled fins, quadratic throttle-authority dependence, hobby-grade actuator dynamics, and gyroscopic effects from high-speed rotor.

## Slide 5
Vehicle Platform: EDF TVC Drone Testbed
5/17
PHYSICAL SPECIFICATIONS
Parameter | Value
Total mass | 3.1 kg
Body length / diameter | 0.35 m / 0.12 m
Ixx, Iyy / Izz | 0.05 / 0.02 kg·m²
EDF unit | FMS 90mm 12-blade
Motor | 4068-KV1850 inrunner
Battery | 6S LiPo
Servos | 4× MG996R
Fin count / area | 4 / 0.002 m² each
Max fin deflection | ±15° (0.262 rad)
Max thrust | 39.2 N
[Insert CAD Render: cad_v1.png]
Control Architecture
● Forward fin (+X): pitch control
● Right fin (+Y): roll control
● Aft fin (−X): complementary pitch
● Left fin (−Y): complementary roll
● Yaw: differential tangential forces
● Altitude: EDF throttle
● → 5 actuators → full 6-DOF control

## Slide 6
Simulation Environment: NVIDIA Isaac Sim
6/17
● Built on Isaac Lab v2.3.2 (PhysX 5 GPU physics)
● 128 parallel environments on a single GPU
● Gymnasium-compatible vectorized interface
● Physics timestep: 8.33 ms (120 Hz)
● RL decision timestep: 33.3 ms (30 Hz, decimation = 4)
● Semi-empirical dynamics models calibrated to hardware
● Two force dispatch modes:
○ Per-link: forces at center-of-pressure locations
○ Collapsed body wrench: for debugging/validation
[Insert: isaacsim_128_env.png 128 parallel environments]
Key Numbers
128
Parallel Envs
120 Hz
Physics Rate
30 Hz
RL Decision Rate
4×
Decimation

## Slide 7
Propulsion Model: EDF Dynamics
7/17
FIRST-ORDER SPOOL + QUADRATIC THRUST
ω̇ = (ω_target − ω) / τ_motor (spool dynamics)
T = k_T · ω² (quadratic thrust)
THREE TORQUE COMPONENTS
● Static reaction torque: τ = −k_Q · ω² (opposes rotor spin)
● Dynamic spool torque: τ = −I_rotor · ω̇ (reaction to acceleration)
● Gyroscopic precession: τ = −ω_body × (I_rotor · ω · ê_z)
○ Couples body rotation to rotor angular momentum
○ Critical for realistic yaw dynamics
EDF PARAMETERS
Parameter | Value
Max thrust T_max | 39.2 N
Motor time constant τ | 0.15 s
Max angular velocity ω_max | 4300 rad/s
Rotor inertia I_rotor | 0.0002 kg·m²
Exhaust speed (nominal) | 116 m/s
Gyro torque scale | 0.1
Key Insight
The gyroscopic precession torque couples body rotation to rotor angular momentum — a real physical effect that makes yaw control non-trivial and distinguishes this from simplified point-mass models.

## Slide 8
Fin Aerodynamic Model: Jet-Vane Forces
8/17
SEMI-EMPIRICAL FORCE MODEL
Dynamic pressure:
q = ½ρ · v²_exhaust · throttle² · k_duct
Normal force coeff:
C_N(α) = C_Nα · α · (1 − k_sat · α²)
Drag coeff:
C_D(α) = C_D0 + C_Dα² · α²
Per-fin forces:
F_n = q · S_fin · C_N(α), F_t = q · S_fin · C_D(α)
Parameter | Value
Air density ρ | 1.225 kg/m³
Exhaust speed v_exh | 116 m/s
Duct correction k_duct | 1.3
Lift slope C_Nα | 3.5 rad⁻¹
Stall saturation k_sat | 2.0
Zero-defl drag C_D0 | 0.05
Drag slope C_Dα² | 1.5
Fin area S_fin | 0.002 m²
CRITICAL COUPLING
Fin force ∝ throttle² — at 50% throttle, fin forces drop to 25% of maximum. This quadratic coupling between thrust and control authority is THE defining challenge of jet-vane TVC and why classical linear controllers struggle outside the hover envelope.

## Slide 9
Learning Algorithm: Proximal Policy Optimization
9/17
PPO WITH CLIPPED SURROGATE OBJECTIVE
L = E[ min( r(θ)·Â, clip(r(θ), 1−ε, 1+ε)·Â ) ]
● On-policy actor-critic algorithm
● Trust-region constraint prevents destructive updates
● Clip coefficient ε = 0.2
● GAE advantage estimation (γ=0.99, λ=0.95)
● Adaptive KL early stopping (KL_target = 0.03)
● Combined loss: policy + value (0.5) + entropy (0.005)
HYPERPARAMETERS (LANDING TASK)
Parameter | Value
Parallel environments | 128
Rollout length | 128 steps
Minibatches / update | 8
Update epochs | 4
Learning rate | 3 × 10⁻⁴
Discount γ | 0.99
GAE λ | 0.95
Clip ε | 0.2
Entropy coeff | 0.005
Max grad norm | 0.5
Why PPO? Robust training stability for continuous control, proven track record in aerial vehicle RL (Koch et al., Hwangbo et al.)

## Slide 10
Observation & Action Space Design
10/17
24-DIMENSIONAL OBSERVATION VECTOR
Index | Component | Dim
0–2 | Position error (m) | 3
3–6 | Attitude quaternion [w,x,y,z] | 4
7–9 | Linear velocity, body FRD | 3
10–12 | Angular velocity, body FRD | 3
13 | Height above ground | 1
14–17 | Fin angles (rad) | 4
18–21 | Fin angular rates (rad/s) | 4
22 | Motor RPM, normalized | 1
23 | Contact state | 1
5-DIMENSIONAL ACTION VECTOR
a = [α₁, α₂, α₃, α₄, u_throttle]
● 4 fin deflections: ±15° (±0.262 rad)
● 1 throttle command: [0, 1]
● Network outputs tanh → linear scaling
● Smaller than quadrotor (typically 4 rotors)
Network Architecture
Actor: Obs(24) → FC(256) → tanh → FC(256) → tanh → FC(5)
Critic: Obs(24) → FC(256) → tanh → FC(256) → tanh → FC(1)
Separate actor-critic networks Learnable per-dimension log-σ for exploration
Design rationale: Quaternion avoids gimbal lock; fin angles/rates give proprioceptive feedback on actuator state (critical given servo lag); normalized RPM informs policy of available fin authority.

## Slide 11
Critical: Initialization Priors on Action Distribution
11/17
1. Throttle Bias Initialization
● Output bias → atanh(2 × 0.78 − 1) ≈ 1.05
● Initial mean throttle ≈ 0.78 (near hover ≈ 0.88)
● Without this: default 0.5 → immediate free-fall
● Agent converges to zero-throttle local optimum
● Physical reasoning: √(mg / T_max) ≈ 0.88
2. Per-Channel Exploration Noise
● Fin channels: log σ = −2.0 (std ≈ 0.14)
● Throttle channel: log σ = −1.0 (std ≈ 0.37)
● Asymmetric: quieter fins, louder throttle
● Prevents lateral oscillations from fin noise
● Maintains altitude exploration range
WITHOUT THESE PRIORS — FAILURE MODES
Default throttle (0.5): → Immediate free-fall → Large negative per-step rewards → Converges to zero-throttle equilibrium → Agent learns: "crash fast = minimize cost"
Uniform exploration noise: → Excessive lateral oscillations from fins → Vehicle destabilized before learning descent → No stable trajectories to learn from → Policy never discovers productive control basin

## Slide 12
Reward Design: Terminal vs. Per-Step Balance
12/17
LANDING TASK REWARD WEIGHTS
Term | Weight
Alive bonus | +0.10
3D position error | −0.05
Horizontal position error | −0.30
Attitude error (tilt) | −0.20
Angular velocity | −0.10
Control effort (fin ¦α¦) | −0.02
Control rate (fin ¦α̇¦) | −0.01
Vertical speed shaping | −0.30
Delta-v cost (T/T_max)² | −0.20
─── Terminal ─── | ───
Crash penalty | −200
Touchdown softness | +25·e^(−v)
Pad accuracy | +200·e^(−d)
Landing success | +250
THE MAGNITUDE BALANCE PROBLEM
For episode length T = 900 (30s at 30Hz): Integrated per-step costs: Σ|w_i|·φ̄_i·T ≈ O(100) If terminal rewards < O(100): → PPO optimizes per-step minimization → Zero throttle = crash fast = minimize cost Solution: Terminal magnitudes (≥200) must clearly dominate integrated per-step budget
Horizontal Guidance Shaping
● Dense lateral gradient (w = −0.30) throughout descent ● Independent of altitude — guides even at high altitudes ● Exponential pad bonus e^(−d) has negligible gradient for d > 2m ● Vertical speed shaping targets ~0.5 m/s descent rate

## Slide 13
Training Procedure & Spawn-Position Curriculum
13/17
TWO TRAINING TASKS
Hover Stabilization
● Residual-PID: PID baseline + PPO correction (scale=0.05)
● 2,048 environment steps, LR = 10⁻⁶
● Rollout: 64 steps, 2 minibatches, 2 epochs
Autonomous Landing
● Pure PPO (no PID baseline) — full trajectory learning
● 5,000,000 environment steps, LR = 3×10⁻⁴
● Rollout: 128 steps, 8 minibatches, 4 epochs
SPAWN-POSITION CURRICULUM
Start (0 steps)
±0.5 m XY spawn box
Learn on-pad touchdown
Linear anneal
±0.5 m → ±2.0 m
Gradually increase lateral offset
End (3M steps)
±2.0 m XY (full range)
Full task difficulty
Altitude
8–12 m (constant)
Same throughout training
Evaluation
Full ±2.0 m range
Always un-curricularized
Rationale: Starting with a narrow spawn box lets the policy learn soft-touchdown behavior first, then generalize to larger lateral offsets. Evaluation always uses the full range.

## Slide 14
Results: Hover Stabilization
14/17
HOVER PERFORMANCE METRICS
Metric | Value | Threshold
Mean position error | 0.085 m | < 0.5 m ✓
Max position error | 0.215 m | < 0.5 m ✓
Mean tilt | < 0.001 rad | —
Max tilt | < 0.001 rad | —
Mean angular rate | 1.1×10⁻⁵ rad/s | —
Evaluation | PASSED | —
Key Findings
● PID provides effective attitude stabilization
● RL residual corrects for position drift
● Only 2,048 steps needed — very fast convergence
0.085 m
Mean Position Error
< 0.001 rad
Mean Tilt
2,048
Training Steps

## Slide 15
Results: Autonomous Landing
15/17
LANDING EVALUATION METRICS (128 PARALLEL EPISODES)
Metric | Value
Landing rate | 100%
Mean touchdown speed | 0.126 m/s
Max touchdown speed | 0.347 m/s
Mean pad distance | 1.89 m
Max pad distance | 4.56 m
Mean throttle (eval) | 0.759
Max downward speed | 9.75 m/s
On-pad fraction (d < 0.5m) | 2%
100%
Landing Rate
0.126 m/s
Mean Touchdown Speed
1.89 m
Mean Pad Distance
5M
Training Steps
✓ 100% landing rate with soft touchdowns — the policy reliably descends and lands safely ⚠ Lateral accuracy remains limited: 1.89 m mean pad distance, only 2% on-pad — the policy has not fully solved lateral guidance to the pad center

## Slide 16
Training Progression & Analysis
16/17
[Insert: training_curves.png Mean Episode Reward over 5M Steps]
TRAINING DYNAMICS
● 0–1M steps: reward ≈ −3 (per-step costs dominate)
● 1–2M steps: transition to positive rewards
● 2–5M steps: steady improvement to ≈ +1.75
● Monotonic upward trend confirms learning
● 100% landing rate achieved early, maintained throughout
Interpreting the Reward Crossover
Negative → Positive crossover at ~2M steps: integrated per-step costs (attitude, control effort, delta-v) give way to terminal landing bonuses (+250 success + up to +200 pad accuracy). This marks when the majority of episodes end in successful landings rather than timeouts or crashes.

## Slide 17
Discussion: The Lateral Accuracy Challenge
17/17
1
Throttle–Fin Coupling
Lateral authority ∝ throttle². During descent, reducing throttle simultaneously reduces fin effectiveness — fundamental tension between descent rate and lateral controllability.
2
Actuator Bandwidth
MG996R servos (τ = 0.05s, 7.54 rad/s max rate) limit correction speed, especially during final approach where rapid corrections are needed.
3
Reward Gradient at Distance
Exponential pad bonus e^(−d) has negligible gradient for d > 2m. Linear horizontal penalty (w = −0.30) may be insufficient vs. vertical/delta-v terms.
4
Curriculum Interaction
Narrow initial spawn helps learn touchdown but may not provide sufficient training signal for large lateral corrections from the full ±2.0m range.
vs. Quadrotors: Independent, throttle-decoupled attitude authority. TVC's coupled control means standard quadrotor RL techniques don't directly transfer.

## Slide 18
Sim-to-Real Transfer Considerations
18/17
Aerodynamic Model Fidelity
Flat-plate fin model may miss flow separation, wake interactions between fins, and ground-effect changes during landing approach.
Mitigation:
CFD validation, wind tunnel data
Servo Nonlinearities
Real MG996R servos exhibit backlash, load-dependent speed variation, and temperature drift not captured by first-order model.
Mitigation:
System identification on hardware
Battery Voltage Sag
6S LiPo voltage drops under load, reducing available thrust during high-throttle maneuvers — not currently modeled.
Mitigation:
Voltage-dependent thrust model
Sensor Noise
Simulation provides clean state observations; physical testbed uses noisy IMU and position estimates.
Mitigation:
Observation noise injection during training
Primary strategy: Domain randomization of aerodynamic coefficients, servo parameters, mass properties, and sensor noise during training to improve transfer robustness.

## Slide 19
Future Work
19/17
GTrXL Policy
Replace feed-forward MLP with Gated Transformer-XL for temporal context — handle wind disturbances and improve trajectory planning during descent. Recent aerospace results (Federici et al., Carradori et al.) show promise.
Domain Randomization
Randomize aerodynamic coefficients, servo parameters, mass properties, and sensor noise during training for robust sim-to-real transfer.
Lateral Guidance
Potential-based reward shaping (Ng et al., 1999), hierarchical policies (separate lateral/vertical controllers), extended curriculum strategies.
Hardware Validation
Deploy trained policies on the physical EDF drone testbed. Validate sim-to-real transfer and characterize the reality gap.
Wind Disturbance Rejection
Train and evaluate under stochastic wind conditions using the simulation's wind model with 27-dim observation space including wind estimates.
Near-term priority: GTrXL integration + domain randomization → hardware flight tests. The 24-dim observation space is already compatible with transformer sequence input.

## Slide 20
Conclusion
PPO can learn thrust-vectored fin control for an EDF VTOL vehicle in simulation — achieving 100% landing rate with soft touchdowns, opening the path to sim-to-real transfer.
KEY CONTRIBUTIONS
✓
GPU-accelerated Isaac Sim environment with semi-empirical aerodynamic, propulsion, and actuator models
✓
PPO hover policy: 0.085 m mean error in only 2,048 steps (residual-PID architecture)
✓
PPO landing policy: 100% success rate, 0.126 m/s mean touchdown speed over 5M steps
✓
Critical insight: initialization priors on action distribution prevent degenerate local optima
✓
Reward design principle: terminal magnitudes must dominate integrated per-step costs
Tang Zijian (Jacob Tang) | Minnesota State University, Mankato
Code & Data: github.com/Jacob19999/Transformer-rl-retro-propulsion
Thank You! Questions?
20/17